# Raspberry Pi LPC1114 I/O Processor LEGO® Power Functions Remote Control
By Philip Munts
Munts Technologies

## Introduction
In The MagPi issue #17, I introduced how to use the LPC1114 analog inputs for sensing the position of an analog joystick. In this article I will show how to control LEGO® Power Function motors with the LPC1114 I/O Processor and how to apply the joystick for controlling a LEGO® RPV (Remotely Piloted Vehicle).
## LEGO® Power Functions Remote Control
LEGO® Power Functions is a system of motors and sensors for the LEGO® system. They can be used with either the traditional LEGO® blocks, or with the newer Technics mechanical components. The motors and sensors can be purchased separately, or as part of a set, such as the LEGO® City train set #7938.
Figure 1 – Some LEGO® Power Functions Components
Left to right: Motors, IR Receiver, Battery Box
The Remote Control IR Receiver #8884 decodes infrared remote control messages in a special coding and sets the speed or position of up to two motors. The receiver is designed to work with the Remote Control #8879. We will be synthesizing the infrared messages with firmware in the LPC1114 I/O Processor to control the IR receiver from the Raspberry Pi instead.
## Infrared Protocol
The IR receiver expects a fairly complex protocol. Fortunately LEGO has published the protocol specification, which can be downloaded from the web page for the #8884 IR receiver. I have added a service to the LPC1114 SPI Agent Firmware that encodes messages for the IR receiver.
Setting up to generate LEGO Power Functions RC messages is easy. First, configure one of the LPC1114 GPIO pins as an output, with the SPIAGENT_CMD_CONFIGURE_GPIO_OUTPUT service. Be sure to initialize the output state to OFF by setting the data field to zero.
Next, generate a message with the SPIAGENT_CMD_PUT_LEGORC service. The data field must be loaded with parameters encoded as follows:
Bits 0-7	Speed:	0-7
Bits 8-15	Direction:	0=Reverse 1=Forward
Bits 16-23	Motor:	0=All stop, 1=Motor A, 2=Motor B
Bits 24-31	Channel:	1-4

See the LPC1114 I/O Processor Expansion Board User Guide (http://munts.com/rpi-lpc1114/doc/UserGuide.pdf) for more information about the SPI Agent Firmware API (Application Programming Interface). The available services are described in detail there.
## Infrared Emitter Circuit
To transmit commands to the IR receiver, you will need to drive an infrared LED (more properly: infrared emitter) from one of the LPC1114 GPIO pins. The GPIO pins can only supply 4 mA of current, which is too little to drive an infrared emitter efficiently. infrared emitters can commonly be driven at 100 mA or more. In order to boost the output current we will use the ULN2003A, a current driver IC that has been around for many years but is still highly useful for this purpose.
The ULN2003A contains 7 amplifiers, or current boosters, each of which can sink 500 mA continuously, or even more for short pulses. Since the ULN2003A is a current sink (pull to ground) device, the cathode (minus) pin of the infrared emitter is connected to the ULN2003A output through a current limiting resistor, and the anode (plus) pin is connected to +5V. (Do not attempt to connect the infrared emitter to +3.3V; the voltage regulator on the Raspberry Pi cannot supply enough current.) See Figure 2 for the infrared emitter circuit.

Figure 2 – infrared emitter Connection
A wide variety of infrared emitters are available, at either 850 or 940 nm wavelengths. Both wavelengths seem to work with the #8884 IR Receiver, but I infer from the color of the filter that it may be optimized for 940 nm. Figure 3 shows a couple of emitters I tried.
Figure 3 – Infrared Emitters – Top: SFH4545, Bottom: SFH4233
The SFH4545 (Digi-Key part number 475-2919-ND) is a 940 nm emitter rated at 100 mA current (pulse), and is representative of what you will find at Radio Shack or other hobbyist sources. This class of device should have a 33 Ω current limiting resistor.
The SFH4233 (Digi-Key part number 475-2910-1-ND) is a very high power 940 nm emitter rated at 1 A current (pulse). This device should have a 3.3 Ω current limiting resistor.
Warning: The combination of the ULN2003A, SFH4233, and 3.3 Ω resistor are capable of generating serious heat if the GPIO pin is left in the ON state. They are capable of melting a solderless breadboard! (Examine the top of Figure 5 below closely for an example...)
## Python3 Test Program
Once the hardware is put together, you can test your setup with the Python3 test program test_legorc.py. It accepts an optional host name parameter, and then 4 numbers (channel, motor, direction, speed). If the motor, direction, and speed are all zero, a panic stop is issued (both motors are stopped immediately).

Example: Show program usage:
./test_legorc.py

Raspberry Pi LPC1114 I/O Processor Expansion Board LEGO Power Functions RC Test

Usage: ./test_legorc.py [hostname] <channel:1-4> <motor:0-2> <forward:0-1> <speed:0-7>

Example: Channel 1, motor 1, forward, speed 1:
./test_legorc.py localhost 1 1 1 1

Example: Panic Stop
./test_legorc.py localhost 1 0 0 0

## Python3 Remotely Piloted Vehicle
For experimentation my son and I constructed a skid steer remote vehicle and wrote a Python program to control it using the analog joystick. A skid steer vehicle has independent motors driving wheels or tracks on either side of the vehicle. Steering is accomplished by driving each side at a different speed and/or direction. See Figure 4.
Figure 4 – Python3 Remotely Piloted Vehicle
The Python3 RPV program test_legorc_rpv.py uses the analog joystick setup from the previous installment in The MagPi #17. The ULN2003A and the SFH4233 infrared emitter have been added to the breadboard. See Figure 4.
Unlike test_legorc.py, which calls C functions in libspiagent.so, test_legorc_rpv.py uses XML-RPC. This simplifies the Python code somewhat.
Figure 5 – Joystick and IR Emitter Hookup
Implementing skid steering in software from a single joystick proved tricky. A certain amount of heuristics (fudge factors) were required.
Useable range for the IR remote control system will vary depending upon the ambient environment and the placement of the infrared emitter. In my office, with a low white ceiling, and using the high power SFH4233, range and coverage are very good as the IR reflects well off the ceiling. At the Helsingborg Raspberry Jam, in an office building foyer with very high ceilings that were dull gray, range was only a few meters with reflected signal. In such circumstances, placing the emitter for line of sight communications instead of relying on reflections would help.
## Links
LPC1114 I/O Processor Expansion Board support info, including how to buy one:	http://munts.com/rpi-lpc1114
LEGO® Power Functions home:	http://powerfunctions.lego.com
ULN2003 datasheet:	http://www.ti.com/lit/ds/symlink/uln2003a.pdf‎
Parallax 2-axis joystick information:	http://learn.parallax.com/KickStart/27800